OpenTRV Code Stack
Outline 2018/02
DHD20180213 V0.1

---
Basic OpenTRV Code Structure
Basic OpenTRV Code Structure
Application
Device declarations, custom + glue logic, sleep loop, polling, stats collection
repo contains several libraries
OTRadioLink repo
(contains several sub-libraries)
Valve support (eg abstract model)
Sensor and actuator support
Radios
Base (eg RTC, sleep and timing support)
Config and h/w setup support
Hardware
MCU, GPIO, sensors, etc

---
Valve Abstraction / Stack
Valve Abstraction / Stack
C++ class AbstractRadValve (and thus an Actuator) is given a target between 0% and 100% open. The % open figure is also sent to any boiler controller listening, and a >= 50% value is construed as a call for heat by the boiler.
Typical layered model in code:
- Model to compute target temperature given occupancy and room history
- Model to compute % open given target and current temperatures
- Driver for (eg) brushed motor with end-stop feedback
- Low level h/w driver controls power to motor via H-bridge(s)